## Slide 1: Data quality verification tools
Verifier overview, Image Feed design, example application
erhtjhtyhy
Barbara Frosik
Principal Software Engineer
Scientific Software Engineering & Data Management
Advanced Photon Source
Argonne National Laboratory
March 20, 2017
In collaboration with beamline 32-ID scientists
Francesco De Carlo
Doga Gursoy
et al

## Slide 2: Thank you
Francesco De Carlo, Doga Gursoy, Rafael Vescovi, Vincent De Andrade; Jun-Sung Park, John Hammomds, Nicholas Schwarz, Arthur Glowacki, Mark Rivers, Tim Madden, Sinisa Veseli, Tekin Bicer
Thank you for great ideas, help, support, consultations.

## Slide 3
Use cases

## Slide 4: Future data processing architecture
http://cbs.fas.harvard.edu/usr/mcmains/CBS_MRI_Quality_Control_Workshop.pdf

## Slide 5: verification
Verifying PVs before start of experiment
Verifying collected hdf data file structure
Verifying collected hdf data
  Frame mean value within limits
  Frame standard deviation within limits
  Frame mean value and mean of means does not exceed delta
32-ID Tomography, Transmission x-ray microscopy, Radiography, Phase contrast imaging

## Slide 6: Blocked projections
For some samples certain projections are blocked, and the characteristic of the corresponding data frames is the same as ‘data dark’.
By applying characteristic (limits) for ‘data’, the blocked frames can be found in a data file and reported. The indexes of blocked frames are used by reconstruction scripts.
32-ID Tomography, Transmission x-ray microscopy, Radiography, Phase contrast imaging

## Slide 7: Detect saturation
The intensity of single points may exceed a limit (saturate)
If there are many of such points, the experiment may be said unsuccessful
The verifier can detect this condition in a data set
With a new detector it may be possible to monitor the data in a real time, so the experiment can be stopped on bad quality
1-ID High-energy x-ray diffraction

## Slide 8: Future data processing architecture
feed
verifier
converter
converter
analyzer
analyzer

## Slide 9
Verifiers

## Slide 10: verifiers
PV – verifies settings of process variables; can be run before experiment, as well as periodically during experiment
Quality results verifiers
  Data verifier – verifies quality of experiment data in a file (hdf, ge, tiff)
  Monitor – monitors directory for experiment data files, and runs data verifier on discovery
  Structure – used for hdf type files. Verifies that the tags are in sync with gathered data.
Real-time – verifies quality of experiment data while experiment is collecting data

## Slide 11: Verifier architecture
handler
aggregate
Experiment
data
frames
results
Data verifier
hdf, ge, tiff
Aggr res
Image feed
frames
real-time
Channel
Access

## Slide 12: Monitoring file system
Experiment
data1
Data verifier1
hdf, ge, tiff
Experiment
data2
Data verifier2
hdf, ge, tiff
Monitor
monitored
folder
observe

## Slide 13: Live feed usage
handler
aggregate
frames
results
aggregated res
Image feed
frames
real-time
Channel
Access
app

## Slide 14: Quality checks
Functions targeted to validate specific experiment data
The checks are configured
Easy to add quality check function to the framework
Check on each frame (ex: mean value expected in certain bounds)
Check on the collected so far frames (ex: number of saturation points exceeded limit)
The same function can be used to assess experiment data taken by different detector by using different limits

## Slide 15: Configuration example
'pv_file' = /home/beams/USR32IDC/.dquality/32id_nano/schemas/pvs.json
'limits' = /home/beams/USR32IDC/.dquality/32id_nano/schemas/limits.json
'quality_checks' = /home/beams/USR32IDC/.dquality/32id_nano/schemas/quality_checks.json
'time_zone' = America/Chicago
'extensions' = .hd5, .HD5, .hdf5, .HDF5, .h5, .H5
#real-time verifier
'feedback_type' = console
'detector' = BBF1
'detector_basic' = cam1
'detector_image' = image1
'no_frames' = 20

## Slide 16: Pv.json
{"S:SRcurrentAI" : {
"greater_than" : 60.0,
"less_than" : 102.0 },
"ID32ds:Energy.VAL" : {
"greater_than": 5.0,
"less_than" : 30.0},
"ID32us:Gap.VAL" : {
"greater_or_equal" : 3.0,
"less_or_equal" : 50.0},
"32ida:BraggEAO.VAL" : {
"greater_or_equal" : 5.0,
"less_or_equal" : 25.0 } }

## Slide 17: Limits.json
{ "data" : {
"mean" : {
"low_limit" : 400,
"high_limit" : 600 },
"stat_mean" : {
"low_limit" : -150,
"high_limit" : 150 },
"std" : {
"low_limit" : 150,
"high_limit" : 200 } } }

## Slide 18: Quality_checks.json
{ “data” :
{ "QUALITYCHECK_MEAN" : ["STAT_MEAN"], "QUALITYCHECK_STD" : []},
“data_white” :
{ "QUALITYCHECK_MEAN" : [], "QUALITYCHECK_STD" : []},
“data_dark” :
{ "QUALITYCHECK_MEAN" : [] }
}

## Slide 19: Verification results
The results are provided in a text file. It lists the result for each frame, and for each check method.
The output of verification is a list of frame indexes that did not pass the quality checks. The list can be used as an input to subsequent calculations.
The real-time verifier provides immediate feedback. Currently the user can choose console and log file. There are plans to add live feedback on the experiment status web page.

## Slide 20: How to use it
Under Documentation Examples tab there are code snippets for each verifier.
  The examples are run with the assumption that a configuration file exists in a folder defined by “instrument”
The github contains another suite of examples in a check.py and check_rt.py files
  dquality.pv.verify(conf)
  dquality.monitor.verify(conf, folder, int(num_files))
  dquality.data.verify(conf, fname)
  dquality.hdf.verify(conf, fname)
  dquality.realtime.real_time.verify(conf, report_file, sequence)

## Slide 21
Live Image feed

## Slide 22: Live Image feed
Uses Channel Access plugin
Uses pyepics
It provides a high level python API to retrieve image data at the time it is recorded
User needs to write defined methods in an adapter.py file and define Area Detector prefixes in a configuration file

## Slide 23: adapter
Acts as a link between feed and consuming application
Has three methods that need to be implemented:
  start_process: it parses arguments, and starts the consuming process. Passes in the queue on which the frames are received.
  parse_config: reads configuration and sets required variables. Since the configuration is specific for the application, it is handled in the adapter.
  pack_data: encapsulates the frame into object defined by a consuming application.

## Slide 24: design
Epics
The Epics can be replaced by other software, ex. Tim Madden’s server
Area Detector
Feed
Consuming Application
Frames, PVs
Q
Enqueue
Frames
Dequeue
Frames

## Slide 25: Adapter for real-time verifier
https://github.com/bfrosik/data-quality/blob/master/dquality/realtime/adapter.py

## Slide 26: links
https://github.com/bfrosik/data-quality
http://data-quality.readthedocs.org/
http://cbs.fas.harvard.edu/usr/mcmains/CBS_MRI_Quality_Control_Workshop.pdf
bfrosik@anl.gov
Contact Barbara Frosik or Nicholas Schwarz for assistance in employing verifier on your beamline

## Slide 27
Questions?
Thank you for your attention